## Slide 1: Packet classification Hierarchical based algorithm
Algorithm implementation in Python
Algorithm performance parameters
Mohammad Ala Amjadi
Person code: 10479915
Master of telecommunication engineering
Politecnico di Milano – September 2020
Professor(s): Achille Pattavina and Guido Maier
Assistant: Sebastian Troia

## Slide 2: Introduction
To meet various QoS requirements, routers need to implement the following features
  Admission control
  Resource reservation
  Per-flow queueing
  Fair scheduling
They need to be able to distinguish and classify the incoming traffic into different flows (flow-aware routers) which is the principle of SDN and OpenFlow
Flows are specified by rules
  Each rule consist of operations comparing packet fields with certain values
A set of rules is called a classifier
  Based on the criteria to be applied to classify packets with respect to a given network application
2
3
1
4

## Slide 3: Network Diagram in general

## Slide 4: A packet classifier example

## Slide 5: Classifier definition
A classifier C consists of N rules, Rj, 1 ≤ j ≤ N, where Rj is composed of three entities:
  A regular expression Rj[i], 1 ≤ i ≤ d, on each of the d header fields of a packet.
  A number, Pri(Rj), indicating the priority of the rule in the classifier.
  An action, referred to as Action(Rj).
An incoming packet P with the header considered as a d-tuple (P1, P2, . . . , Pd) is said to match Rj , if and only if, Pi matches Rj[i], where 1 ≤ i ≤ d.
Given an incoming packet P and thus the d-tuple, the d-dimensional packet classification problem is to find the rule Rm with the highest priority among all the rules Rj matching the d-tuple
An IPv4 packet header, consists of:
  Source IP 32bits
  Destination IP 32bits
  Protocol 8bits
  Source port 16bits
  Destination port 16bits
The matching rule in the classifier with the highest
priority is chosen and its corresponding action is
applied to the packet

## Slide 6: Classifier table example
Each rule has five regular expressions on five packet-header fields from network layer to application layer
Each expression could be:
  Simple prefix/length specification => Same definition as in P lookups
  Operator/number specification => could be more general, such as equal 23, range 256-1023, and greater than 1023
A wildcard can be inserted to match any value.
Note R4 ‘all-wildcards’ specification => matches with any incoming packet
  The priorities of rules take effect when a packet matches both R4 and other rules

## Slide 7: Program structure
Hierarchical_algorithm.py main algorithm functions
Network_utils.py customized general functions and rules
main.py program to run the algorithm
rule_list.txt classification rule list
random_packets.txt randomly generated incoming packets list
incoming_packets.txt customized incoming packets list

## Slide 8: Flow – Construct Rule Object and all_rule List
First, we read the rule list using read_rules() function. Inside this function we go over each line of our text file (rule_list.txt) and create an object Rule. In Rule object we have all the information that we need in separate attributes. The binary format of the prefixes will be calculated using extract_info() function. If the NetID in the rule list has a * (star) value, the src_sub_binary or dst_sub_binary attribute will remain as None. All the object rules will be added to a list called all_rules.
class Rule:
src_sub = None
src_ip = None
src_netmask = None
src_sub_binary = None
dst_sub = None
dst_ip = None
dst_netmask = None
dst_sub_binary = None
src_port = None
dst_port = None
protocol = None
action = None

## Slide 9: Flow
First, we read the rule list using read_rules() function. Inside this function we go over each line of our text file (rule_list.txt) and create an object Rule. In Rule object we have all the information that we need in separate attributes. The binary format of the prefixes will be calculated using extract_info() function. If the NetID in the rule list has a * (star) value, the src_sub_binary or dst_sub_binary attribute will remain as None. All the object rules will be added to a list called all_rules.
def __init__(self, src_sub, dst_sub, protocol, src_port, dst_port, action):
self.src_sub = src_sub
self.dst_sub = dst_sub
self.protocol = protocol
self.src_port = src_port
self.dst_port = dst_port
self.action = action
if self.src_sub is not '*':
self.src_ip, self.src_netmask, self.src_sub_binary = extract_info(self.src_sub)
if self.dst_sub is not '*':
self.dst_ip, self.dst_netmask, self.dst_sub_binary = extract_info(self.dst_sub)

## Slide 10: Flow
First, we read the rule list using read_rules() function. Inside this function we go over each line of our text file (rule_list.txt) and create an object Rule. In Rule object we have all the information that we need in separate attributes. The binary format of the prefixes will be calculated using extract_info() function. If the NetID in the rule list has a * (star) value, the src_sub_binary or dst_sub_binary attribute will remain as None. All the object rules will be added to a list called all_rules.
Then the root Node object will be created. This has some attributes which will help us to implement the tree. Each node has a value, zero, one, dst_root, end and node_rules attribute. The value attribute is used to better understand the tree and draw it. By default the end attribute is False and if it becomes True it means we have reached the end of the tree.
value = “^” The main root node
value = “#” Second tier root node
value = “$” The last node of second tier
The dst_root will be used for the first node of second tier that becomes as a root of the new tree in the second tier. node_rules is a list of all the rules were a match for this node. one and zero attributes are obviously the binary tree arcs that we have.
class Node:
value = None
zero = None
one = None
dst_root = None
end = False
node_rules = None
def __init__(self, value="^", end=False):
self.value = value
self.end = end
if self.end:
self.node_rules = []

## Slide 11: Flow
src_sub_binaries and dst_sub_binaries contains only the binary values of the rules which can be extracted from all_rules list. These two new list may contain None value in case that we had * (star) as source or destination NetID.
src_sub_binaries = [x.src_sub_binary for x in all_rules]
dst_sub_binaries = [x.dst_sub_binary for x in all_rules]
By iterating over these two new lists we can start our algorithm by calling the add_src_nodes() function. This function receives a node as reference and two src_sub_binaries and dst_sub_binaries lists, and it has two indexes. The index is used for tracking the number of bits that we have covered so far. The rule_index is used in the iterations as the priority number of the rule in the all_rules list.
for i in range(0, len(src_sub_binaries)):
bt.add_src_nodes(root, src_sub_binaries[i], 0, dst_sub_binaries[i],i)

## Slide 12: Flow
def add_src_nodes(node, src_rule, index, dst_rule, rule_index):
if src_rule is None:
src_rule=[]
if len(src_rule) <= index :
if dst_rule is None:
if not node.end:
node.node_rules = []
node.end = True
node.node_rules.append(rule_index)
return
if node.dst_root is None:
node.dst_root = Node(value="#")
add_dst_nodes(node.dst_root, dst_rule, 0, rule_index)
return
if src_rule[index] == "0":
if node.zero is None:
node.zero = Node(value=(node.value + "0"))
add_src_nodes(node.zero,src_rule, index+1, dst_rule, rule_index)
else :
if node.one is None:
node.one = Node(value=(node.value + "1"))
add_src_nodes(node.one,src_rule, index+1, dst_rule, rule_index)

## Slide 13: Flow
def add_dst_nodes(node, dst_rule, index, rule_index):
if len(dst_rule) <= index :
if node.zero is None:
node.zero = Node("$",end=True)
if not node.zero.end :
node.zero.end = True
node.zero.node_rules = []
node.zero.node_rules.append(rule_index)
return
if dst_rule[index] == "0":
if node.zero is None:
node.zero = Node(value=(node.value + "0"))
add_dst_nodes(node.zero,dst_rule, index+1, rule_index)
else :
if node.one is None:
node.one = Node(value=(node.value + "1"))
add_dst_nodes(node.one,dst_rule, index+1, rule_index)

## Slide 14: Flow – Construct Rule Object and all_rule List
Then, we read the packet list using read_packets() function. Inside this function we go over each line of our text file (packets.txt) and create an object Packet. In Packet object we have all the information that we need in separate attributes. The binary format of the IP addresses will be calculated using ip_to_binary() function. All the object packets will be added to a list called packets.
class Packet:
src_ip = None
dst_ip = None
protocol = None
src_port = None
dst_port = None
src_binary = None
dst_binary = None
def __init__(self, src_ip, dst_ip, protocol, src_port, dst_port):
self.src_ip = src_ip
self.dst_ip = dst_ip
self.protocol = protocol
self.src_port = src_port
self.dst_port = dst_port
self.src_binary = ip_to_binary(src_ip)
self.dst_binary = ip_to_binary(dst_ip)

## Slide 15
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Average time (ns) | 8029 | 5438 | 4702 | 4598 | 4529 | 4312 | 5456 | 4911 | 4510 | 6304 | 5050 | 4577 | 5843 | 4481 | 4334 | 4489 | 6669 | 4654 | 4555 | 4856 | 4707 | 4426 | 4434 | 4366 | 4426 | 4467 | 4838 | 4452 | 5854 | 4829 | 6575 | 5011
Test was performed each time with 100.000 packets and 100 Rules.
Since the packets were generated randomly and there was only 100
Matches per each test, backtracking didn’t happen and the average
times are very close to each other and the median average time for
each packet is 4678 ns.

## Slide 16: Performance Evaluation – Time
Chart: 
| 1 | 10 | 100
Time (ms) | 2334 | 6064 | 14425
Search Speed (Classification time):
The total classification increases linearly with the incoming packets
Storage requirement (memory):
evaluation was not successful since the outcome measurements were inaccurate.
Scalability:
Size: classified 1 Million entries in 14425 ms
Header fields: this program doesn’t accept dynamic dimension of classifiers.
Update time:
This program doesn’t consider updates of rules in its algorithm.
Flexibility in specification:
This program accepts NetID and ranges for port numbers.
Using different NetID increased the classification time. Using port ranges instead
of numbers did not increased the classification time significantly.
Chart: 
| 100 | 1000 | 10000 | 100000 | 1000000
Time (ms) | 0 | 15 | 145 | 1676 | 14425

## Slide 17: End
Questions?